## Slide 1: Memory for VLA
Seokmin Lee
2026.07.02

## Slide 2: contents
Previous Approaches
Experimental Settings
Ideas

## Slide 3: Previous Approaches

## Slide 4: Previous Approaches
In General, There are two types of Memory
  Symbolic memory (with Planner)
  Perceptual memory (without Planner)

## Slide 5: Symbolic Memory – hierarchical structure
Dino v2
Current Image
“grasp the blue cube, move left, grasp the yellow cube …”
tokenizer
Subtask history
Our final Goal is "clean the desk“.
What is next subtask?
tokenizer
VLM
“put yellow cube into the bin”
Next subtask
VLA
“put yellow cube into the bin”
Next subtask
Dino v2
Current Image
tokenizer
Action
chunk

## Slide 6: Symbolic Memory – hierarchical structure
Planner is called at every iteration
Action chunking keeps VLM latency affordable
  But still have latency issue : latency critical tasks
Predicted subtasks are accumulated in the subtask history
Consecutive duplicate subtasks are removed

## Slide 7: Robomme - symbolic, simple
Generate subtasks without grounding to the target.
Limited performance ceiling.

## Slide 8: Robomme - symbolic, grounded
Follows the standard subtask generation pipeline (shown below).
Extends each subtask with the target object's image coordinates.
  Example: Put the yellow cube at [120, 10] into the bin.
Requires additional annotation for target grounding.

## Slide 9: Robomme - symbolic, grounded
High performance with a latency-free oracle planner.
A low-latency, accurate planner is sufficient without modifying the VLA.
Existing VLM planners (e.g., Gemini, Qwen) are still inadequate.
  Planner latency, weak grounding, and subtask prediction errors remain major bottlenecks.

## Slide 10: MEM (Physical intelligence)
Introduces a video encoder with causal temporal attention.
History summarization

## Slide 11: Perceptual Memory
VLA
“clean the desk”
Final Goal
Dino v2
past Image
tokenizer
Action
chunk
Dino v2
past Image
Dino v2
past Image
Dino v2
past Image
Dino v2
current Image

## Slide 12: Perceptual Memory
Store past keyframes or uniformly sampled frames as memory.
No VLM planner latency.
The key challenge is identifying which frames are worth storing.
  Action loss provides an extremely sparse supervision signal for keyframe selection.
  Manual keyframe annotation is not scalable.

## Slide 13: Robomme – perceptual, sampling
Uniformly samples past frames as memory.
Current state-of-the-art memory strategy.

## Slide 14: Memory VLA (ICLR 2026)
No qualitative analysis
Limited ablation studies
No evaluation of whether the retrieved frames are actually informative or relevant
Compared only against naïve baselines

## Slide 15: MemER (ICLR 2026)
Planner predicts keyframes.
Requires keyframe annotations.
  Scalability is limited by the need for manual annotations.

## Slide 16: Experimental Settings

## Slide 17: Experimental Settings : Training
Training : 4 x A100 GPUs
  Planner training : unexpected performance issue; training log is different from author’s one.
  VLA training : Running well.
    PCI (~2 days) : evaluation success
    Nvlink : issue is resolved & Training in progress.

## Slide 18: Experimental Settings : Evaluation
Evaluation : 2 x RTX 4090 GPUs
  Both the planner and VLA run without issues.
    Planner : 1~1.5 days
    VLA : 4~5 hours

## Slide 19: Evaluation Settings : ToDo
Successfully train Planner is the only thing we should do

## Slide 20: Ideas

## Slide 21: Ideas – Perceptual
Can a perceptual memory system identify informative past frames using only sparse supervision?
  Enabling reliable keyframe selection from sparse learning signals could have significant research impact.
If not, explicit keyframe annotations may be necessary.
  While this is justifiable—similar to symbolic approaches that require subtask annotations—the scalability of manual keyframe annotation remains an open question.

## Slide 22: Ideas – Symbolic
If we pursue a symbolic approach, the grounded planner should be modular rather than relying on a monolithic VLM.
Instead of invoking the planner at every iteration, trigger it only when necessary (e.g., upon detecting meaningful events or uncertainty).
The upper performance bound is promising, making this direction worth exploring.
Alternatively, an agent-based planner may be a better fit.
Using a full VLM as the planner feels excessive for this role.

## Slide 23: The End